Royal Society Short Industrial Fellowship Project Progess Update
Update at 06 July 2023
- Implement EMPC into C++ and integrate into Autoware.AI mpc package
- Add recent work into github repository
- Other work to be done

---
EMPC implementation
- EMPC design procedure
  - Decide the operation condition for this EMPC to work on (speed and curvature)
  - Decide the vehicle model, model parameters and constraints to use
    - Kinematic model for low speed
    - Dynamic model for high speed
    - Decide the constraints
  - Decide the MPC design parameters
    - N - prediction horizon
    - Q – weight on states
    - R – weight on control
  - Use the MPT3 toolbox to compute the EMPC controller.
    - A MATLAB script is provided to do this
      calculateEMPC(modelType, model_param_, mpc_param_, operat_cond_, dt)
    - It outputs a EMPC function in C++ ’empc_solution.cpp’ empc_solution_pQP1_ff_KinematicsBicycleModelWithDelay(const Eigen::VectorXd& x, const Eigen::MatrixXd& H, const std::vector<int>& ni, const Eigen::MatrixXd& fF, const Eigen::MatrixXd& tF, const std::vector<double>& tg, const Eigen::MatrixXd& tH, const Eigen::MatrixXd& fg, const int nz, const int nr)
    - Inputs to the EMPC function are system states (eg. lateral deviation, heading error, steering angle …) and a set of pre-computed parameters (i.e. H, ni, fF, tF, tg, tH, fg, nz, nr..) which are generated by ‘calculateEMPC’ script and saved in csv files.
  - Move ‘empc_solution.cpp’ and folder ‘empc_data’ which contains the pre-computed empc parameters to ASLAN’s corresponding folders
  - Build ASLAN and ready to go
- Current Design
  - Operation condition:
    - Speed 3 m/s
    - Curvature 0.01 1/m
  - Kinematic model with steering delay
  - Constraints
    - Steering limit <40 deg
    - Lateral error < 1 m
  - MPC design parameters
    - N = 70
    - Q = 0.1
    - R = 1
    - Sampling time = 0.1s
  - EMPC region numbers: 438
  - Estimated storage size: ???

---
MPC and EMPC results comparision
- Online MPC
- EMPC

---
Github repository
- Created a forked repository of Aslan in my Github account
- Create a branch named mpc_test
  - In the mpc_test branch, I uses the ground truth of vehicle pos as inputs. After testing, will create a new branch name ‘mpc’ which use inputs from NDT localisation as it is original Aslan
- Push the all my recent work to mpc_test branch
https://github.com/Qian628/Aslan.git

---
Add MPC and EMPC option into Aslan GUI

---
Other work to be done
- Design EMPC for other operation conditions (speed vs curvature)
- Estimate the storage size for full EMPC for all operation conditions
- Restore the inputs to MPC/EMPC to NDT localisation outputs
- Test them at MIRA test track
- Documentation
  - Include add readme file to the repository
- Merge the work to Aslan
- Support needs from SD
  - A measurement of steering position is to be added to the vehicle interface
  - To check the current lidar logs taken from MIRA tracks to see if a useable map can be created.